## Slide 1: BIII – Lattice design
LIMITS OF
MBA–LATTICES WITH REVERSE BENDS
USING SEPERATED FUNCTION MAGNETS
PART II
Bettina Kuske, 11-2020

## Slide 2: Content
Structure of this talk:
Short recapitulation of last talks results
Matching cell
Further boundary conditions
  Restrictions on a
  Restrictions of normalized chromaticity
Options to relax previous boundary conditions in order to meet new ones
Lattice options for BIII

## Slide 3: Summary last talk I
„Prototype“ lattices:
  Typical lattice solutions that emerge from certain boundary conditions
Standard MBA lattices:
(using separated function magnets and reverse bends)
Achromatic arc: identical MBA-cells and 2 matching cells at each end
Optimization criteria:
  TME: theoretical minimal emittance
  minimal circumference
  (TME conditions are an important ‘anchor’ in the multi-parameter space)
Development of MBA-cell can follow “deterministic procedure”
  Half MBA-cell: Transfer line with “TME” initial conditions (bx, hx)
  QF, QD and reverse bend angle to fit ax = ay = h'x = 0 @end
Reverse bend: negligible impact on e, needed for compactness
Hardware: Maximal fields and gradients (B~1.5T, G<100T/m), equal drifts of 0.1m

## Slide 4: Summary last talk II
Smallest emittance is not of highest priority 
  5 bend achromat (3MBA-cells) and 20 periods:
But: results hold for 16 and 18 periods as well
  (different combination of very similar structures)
 |  | # achromats / straights 16 18 20 |  | 
MBA-cell/arc |  | 5 | 4 | 3
Angle main-dipole | [°] | 2.0 | 2.15 | 2.4
Circumference | [m] | 332 | 333 | 327
Emittance | [pm rad] | 66 | 80 | 112
Efficiency (free space / circ) | [%] | 24 | 27 | 30
LER workshop 2020, link to talks: https://agenda.infn.it/event/20813/timetable/#20201026.detailed
Efficiency: SLS2: 17%, Soleil2: 45%, Elettra: 30%, Diamond: 25%

## Slide 5: Requirements for matching cell
Tasks of matching cell:
Suppress dispersion
Fit beta functions in straight section: injection, optimal conditions for experiment
Need high degree of flexibility
As short as possible (1/2 MBA-cell)
h = h’ = 0
Matching-cell
hx
Dispersion suppressor
½ MBA-cell
Last MBA-cell
Matching to straight section

## Slide 6: matching cell with reverse bend, 5-bend, 20 periods (last talk)
L = 4.74m
(1.13 + 1.11+2.5m)
𝜀 = 108pmrad
𝜉x = -3.4
𝜉y = -1.2
𝜑x = 174.4°
𝜑y = 12.9°
bx = 12.5m
by = 8.7m
bx
hx
by
Problem: MQD, MQF, UQ1, UQ2, UQ3 – 5 knobs
need to fit , ‘,  x, y, x, y - 6 parameters
Initial conditions fixed by MBA-cell for bx, by, hx (ax = ay= h'x = 0)

## Slide 7: “Extended” matching cell
L = 5.93m
𝜀 = 104pmrad
𝜉x = -5.2
𝜉y = -1.3
𝜑x = 320.8°
𝜑y = 89.3°
bx = 1.5m
by = 1.5m
bx
hx
by
Solution: use ‚QFA‘ (focusing) quadrupoles of last MBA-cell:
No (significant) change of emittance
Long leaver – small changes in field
DK(QFA) ~ 1% for 1.5m < bx < 17m
‘QDA’ defocussing – not effective
½ last MBA-cell
Matching-cell

## Slide 8: Flexibility of the Matching section
bx [m] | by [m] | Qx | Qy | xx | xy | [pm] | K > 12 [1/m²]
1.5 | 1.5 | 54.8 | 11.5 | -322 | -88 | 111 | 
3.0 | 3.0 | 52.7 | 9.9 | -312 | -81 | 113 | MQ2 1.6%
5.0 | 5.0 | 51.2 | 8.1 | -310 | -81 | 112 | 
11.0 | 3.0 | 49.6 | 9.1 | -312 | -89 | 110 | UQ1 3%
17.0 | 7.0 | 49.1 | 6.2 | -313 | -104 | 109 | UQ1 20%
 |  | D 5.7 | D 5.3 | +/-2% | +/-13% | +/- 2% | 
Soleil injection
values
SLS2 injection
values
Fitting different beta functions in straight section:
no optimization of dynamic aperture at this stage, only crude verification of few initial mm.
JB: 1.5-2m for 3-4m undulator
SLS2 injection betas
bx, = by = 1.5m

## Slide 9: Reverse bend in matching cell
Reverse bend not needed in matching cell
  h’ = 0, but no conditions on ax, ay at end of bend
  Use MQF, MQD to fit h = h’ = 0
  Saves 0.15m*40=6m circumference
  Emittance decreases (reduced angle in bend)
  a increases
9
h = h’ = 0
Matching-cell
hx
Keep all other elements (at this stage):
Quadrupoles to provide knobs for fitting
Sextupoles to make chromaticity compensation more flexible

## Slide 10: Prototype lattice 5 bend 20 periods
L = 16.06m 𝜉x = -307 Qx = 54.25 e = 105pmrad
C = 321.2m 𝜉y = -89 Qy = 11.35 a = 0.14e-4
“Norm. chromaticity”: 𝜉x /Qx = ~5.7, 𝜉y /Qy = ~7.8
“Best” lattice: 5-bend MBA with 20 straight sections, separated function magnets:
“Reference lattice” for the rest of the talk
Shortest, separated function magnet lattice-type
with ~100pm and 20 straight sections.
(non-hybrid MBA)

## Slide 11: Prototype lattice 5 bend 20 periods
Dynamic Aperture – stage 0 – 1000 turns
Qx=54.25, Qy=11.35
Chromaticity tuned to +2
6 SX families: SD/SF in MBA cell
        SDA/SFA in matching cell
        S3,S4 in straight section
OPA – optimization tune shift terms
=> Promising start for optimization
@ center of
straight section
bx = 1.5m
by = 1.5m

## Slide 12: Further boundary conditions
  Limitation of normalized chromaticity
    => off momentum properties
  (A. Streun: „gut-feeling“– should be rather 3 than 10,
  J. Bengtson: „Chromaticity wall“)
Other labs / lattices obey two further constraints:
  Limitation on a (SLS2, Soleil: a > 1e-4)
    => Touschek lifetime, instabilities, orbit stability
  Increase h, q in main bend
  Decrease h, |q| in reverse bend
Reference lattice 5 bend MBA, 20 periods:
a = 0.14e-4  1e-4 factor ~7
Norm. chromaticity:
𝜉x /Qx = ~5.7, 𝜉y /Qy = ~7.8  𝜉/Q = ~3 factor 2-3
=> decrease bx, by
X
X

## Slide 13: Relaxation of boundary conditions
    Gradient in reverse bend
  3. Increase L - main dipole length
    Keep TME-emittance (?)
  Use combined function magnets:
    4. Gradient in main dipole (TG, LG)
Relaxation of boundary conditions – what do we gain?
  Relax TME-condition on h
  Relax TME-condition on bx
costs emittance,
reversible
fixed gradients, not tunable!
Apply options to reference optics and investigate their impact :
  on
  on normalized chromaticity
Option concern MBA-cell, matching cell needs to be adjusted
Constraints on drifts, fields, gradients not studied in this context (technical)
Combined function magnets: loss of incorporated steering/multipole options

## Slide 14: 1 - Relax TME-condition on h
Findings MBA-cell:
keep total angle
Reverse bend kick decreases
main bend 2.39° ↘ 2.31°
a increases
Emittance increases ^2 ( )
Norm. chrom. unchanged
  (only by changes due to
  edge focusing, matching
  cell stays the same.)
reference input (MBA-cell):
Half length dipole: 23cm
Half angle m-bend: 2.39°
Rev. bend angle: -0.205°
TME-b: 0.0594m
TME-h: 0.0016m
reference output
(MBA-cell):
e: 114pm
a: 0.08e-4
xx/ Qx : -6.1
xy/ Qy : -19.4
Main bend: 2.39°…. 2.31°
reference output
(matching-cell):
e: 97pm
a: 0.13e-4
xx/ Qx : -5.8
xy/ Qy : -5.9
reference output
(full lattice):
e: 105pm
a: 0.14e-4
xx/ Qx : -5.7
xy/ Qy : -7.8

## Slide 15: 1 - Full lattice with relaxed dispersion
MBA-cell:
h0 = 0.003m
q = 2.32°
qR = -0.11°
e = 160pm
a =1.01e-4
eMatching-cell:*
= 2.37°
qR = 0°
e = 118pm
a = 0.32e-4
Full lattice:
e = 140pm (105pm)
= 0.52e-4 (0.14e-4)
xx/ Qx = -5.7 (-5.7)
xy/ Qy = -7.8 (-7.8)

But: need to consider matching cell, too:
*: e-matching cell includes half bend and reverse bend from last MBA-cell
=,h = 0 in straight section => h is small in matching dipole => is small
q is fixed by MBA-cell, length is minimal
1 – Increase h0 from TME-value:
good way to increase a, but not sufficient
limited by emittance growth
no impact on normalized chromaticity (MBA-cell)

## Slide 16: 2 - Relax TME-condition on bx
~ opposite to increase of h:
Reverse bend kick increases
a decreases < 0
Emittance increases
reference input (MBA-cell):
Half length dipole: 23cm
Half angle m-bend: 2.39°
Rev. bend angle: -0.205°
TME-b: 0.0594m
TME-h: 0.0016m
reference output
(MBA-cell):
e: 114pm
a: 0.08e-4
xx/ Qx : -6.1
xy/ Qy : -19.4
reference output
(matching-cell):
e: 97pm
a: 0.13e-4
xx/ Qx : -5.8
xy/ Qy : -5.9
reference output
(full lattice):
e: 105pm
a: 0.14e-4
xx/ Qx : -5.7
xy/ Qy : -7.8

## Slide 17: 2 - Relax TME-condition on bx
Full lattice:
e = 139pm (105pm)
= 0.06e-4 (0.14e-4)
xx = -188 (-307)
xy = -60 (-89)
xx / Qx = -3.5 (-5.7)
xy / Qy= -3.9 (-7.8)
Half MBA-cell:
h0 = 0.0016m
bx0 = 0.12m
by0 = 8m
= 2.39°
qR = -0.235°
e = 145pm
a =-0.08e-4
xx / Qx = -3.2
xy / Qy= -6.1

Abs (norm. chromaticity) shrinks
2 – Increase bx from TME-value:
reduction of (normalized) chromaticity
increase in sextupole strength up to 50% - due to smaller beta functions
No ‘break through’ in dynamic aperture
Normalized chromaticity

## Slide 18: 3 - Increase dipole length - keep TME-condition
Findings MBA-cell for increased dipole length:
Emittance contribution of RB
Impact of reverse bend on emittance
  not negligible anymore
TME conditions not optimal ?
Half dipole: 2.39°, 0.23m  0.40m
Field: 0.87T
TME: bx0 = 0.103m (0.0594m)
h0 = 0.0028m (0.0016m)
e

## Slide 19: 3 - Increase dipole length – restore minimal Emittance
  Keep bx0 = 0.103m (TME)
  - Keep cell deflection angle const.
Change h0 to recover TME-emittance:
Starting point
Minimize emittance (-8pm)  keep emittance but increase a *7

## Slide 20: 3 - Increase dipole length – Full lattice
Full lattice: Ref.
e = 121pm (105pm)
a = 0.38e-4 (0.14e-4)
xx / Qx = -4.6 (-5.7)
xy / Qy= -6.2 (-7.8)
Circ. = 339.6 (321.2)
3 – Increase dipole length
emittance contribution of RB not negligible
full lattice: a = 1.0e-4  e = 158pm
+ 18m circumference
  option for combined function magnets
MBA-cell: (Ref.)
e = 119pm (114pm)
= 0.60e-4 (0.08e-4)
Half main bend:
LMB = 0.40m
= 2.345°
qR = -0.25°
h0= 0.0035m
Full lattice: Ref.
e = 125pm (105pm)
a = 0.58e-4 (0.14e-4)
xx / Qx = -4.6 (-5.7)
xy / Qy= -6.2 (-7.8)
Circ. = 339.6 (321.2)
MBA-cell: (Ref.)
e = 126pm (114pm)
= 1.00e-4 (0.08e-4)
Half main bend:
LMB = 0.40m
= 2.3°
qR = -0.205°
h0= 0.0043m
Minimize emittance:
Maximize a:
factor 4 in a with moderate increase in e (16%)
reduction in norm. chrom.

## Slide 21: 4a - Increase dipole length + include transverse gradient
MBA-cell: (long dipole)
e = 137pm (126pm)
= 2.15e-4 (1.03e-4)
Half main bend:
LMB = 0.40m
= 2.3°, 0.84T
K = -2.28m-², -19T/m
h0 = 0.0059m
by0 = 9m
qR = -0.215°
Include QD in main bend:
Effect of transverse gradient (TG) in main dipole:
Practical: gradient cast in dipole profile – fixed
QD: h, bx (emittance) increases
Damping partition number > 1
a increases
Save circumference
emittance reduction?
Full lattice: (Ref.)
e = 134pm (105pm)
= 1.01e-4 (0.14e-4)
xx/Qx = -3.8 (-5.7)
xy/Qy = -3.4 (-7.8)
Jx = 1.22 (1.0)
Circ: = 318.8m (321.2m)


## Slide 22: 4a - Increase dipole length + include transverse gradient
Check the impact of h0 in main bend:
4A – TG in long main dipole
Sufficient increase in a
Strong reduction in chromaticity (small b, h increase sextupole strength)
Moderate increase in emittance
Circumference ok
: best choice

## Slide 23: 4b – LONG Main bend with longitudinal gradient
LGB:
basic idea:
Optimization module in OPA for longitudinal bends
Even 2 field levels with equal length lead to emittance reduction of 26%!
B [ T ]
L [m]
Further option to reduce length of central part
and increase field not yet invested
B [ T ]
L [m]
B [ T ]
L [m]

## Slide 24: 4b – LONG Main bend with longitudinal gradient
Dipole with LG, two field levels:
Small minimal emittance => higher increase for large a
: best choice

## Slide 25: 4b – LONG Main bend with longitudinal gradient
Full lattice (single long dipole):
e = 125pm
= 0.58e-4
xx/Qx = -4.6
xy/Qy = -6.2
Circ. = 339.6
Half MBA-cell
(single long dipole):
= 2.3°
qR = -0.205°
h0 = 0.0043m
bx0 = 0.103m
by0 = 12m
Two parts 0.2m:
q = 2.3° (1.5°/0.8°)
qR = -0.205°
h0 = 0.0031m
bx0 = 0.103m
by0 = 12m
Full lattice: (Ref.)
LG
e = 108pm (105pm)
= 0.40e-4 (0.14e-4)
xx/Qx = -4.6 (-5.7)
xy/Qy = -5.5 (-7.8)
Circ: = 340.4m (321.2m)
Half MBA-cell: (single long
LG dipole):
e = 95pm (126pm)
= 0.64e-4 (1.03e-4)
xx/Qx = -4.5 (-4.5)
xy/Qy = -11.3 (-11.2)
4B – LG in long main dipole
Can seek very small emittance at negative a
Full lattice: a = 1.0e-4  e = 179pm

## Slide 26: 5 - include transverse gradient in reverse bend
Transverse gradient (TG) in reverse bend:
Realization as displaced quadrupole (QF)
No change in main bend 2.39°, L=0.23m
(TME: bx0 = 0.0594m, by0 = 15m, h0 = 0.0016m)
Jx > 1 => emittance reduction
Reduction of circumference 18m (0.15*6*20)
: best choice

## Slide 27: 5 - include transverse gradient in reverse bend
QF/reverse bend:
qR = -0.215°, 0.22T
LR = 0.14m
K = 11.1m-², 92T/m
Include QF in reverse bend :
Full lattice: Ref.
e = 84pm (105pm)
= 0.14e-4 (0.14e-4)
Jx = 1.13 (1)
xx/Qx = -6.1 (-5.7)
xy/Qy = -7.7 (-7.8)
Circ: = 304.0m (322.4m)

MBA-cell:
= 84pm (114pm)
= 0.11e-4 (0.08e-4)
Jx = 1.25 (1.0)
Effect of gradient in reverse bend on emittance is ~25% reduction due to Jx
5 – Displaced QF
Tool to reduce emittance and circumference
Full lattice: a = 1.0e-4  e = 254pm  no reverse bend

## Slide 28: Comparison of 5 options to relax the MBA-cell
 | Results for full lattices | e [pm] | a [e-4] | x/ Q x | x/ Q y | q RB | Circ. [m]
 | reference | 105 | 0.14 | -5.7 | 7.8 | -0.205 | 321.2
1 | Relax h0 | 140 | 0.52 | -5.7 | -8.7 | -0.110 | 321.2
2 | Relax b0 | 139 | 0.06 | -3.6 | -3.9 | -0.235 | 322.8
3 | Increase L | 135 | 0.74 | -4.6 | -6.2 | -0.165 | 339.6
4a | Increase L + TG | 134 | 1.01 | -3.8 | -3.4 | -0.205 | 318.8
4b | Increase L (+LG) | 142 | 0.74 | -4.6 | -5.6 | -0.165 | 338.8
 |  | 98 | 0.12 | -4.6 | -6.3 | -0.265 | 339.6
5 | Displaced QF | 135 | 0.62 | -6.0 | -8.4 | -0.095 | 304.0
 |  | 84 | 0.14 | -6.1 | -7.7 | -0.215 | 304.0
Separated function magnet lattices do not seek a > 1e-4 with emittance ~100pm
Long bend most promising (a = 0.99e-4, e = 158pm)
Separated
function
magnets
A long main bend w/, w/o gradient seeks highest a values
Both, 4b and 5 can also be used to lower the emittance
=> Combination of measures needed

## Slide 29: comparison of dipole options
a ~2e-4 and e ~100pm not possible with single measure
The original short bend is worst solution
Long bend and TG improve alpha, LG and TG-RB improve emittance
Fun fact: identical dependence of LG and TG-RB, but at different bend angles
@ ~130pm, a ~ 1e-4 achievable with all methods (but short bend)
 corresponds to a ~ 0.6e-4 , e ~125pm (full lattice)
Values for MBA-cell (not full lattice)

## Slide 30: lattice combining options 4a and 5
 | Results for full lattices | e [pm] | a [e-4] | x/ Q x | x/ Q y | q RB | Circ. [m]
 | reference | 105 | 0.14 | -5.7 | 7.8 | -0.205 | 321.2
1 | Relax h0 | 140 | 0.52 | -5.7 | -8.7 | -0.110 | 321.2
2 | Relax b0 | 139 | 0.06 | -3.6 | -3.9 | -0.235 | 322.8
3 | Increase L | 135 | 0.74 | -4.6 | -6.2 | -0.165 | 339.6
4a | Increase L + TG | 134 | 1.01 | -3.8 | -3.4 | -0.205 | 318.8
4b | Increase L (+LG) | 142 | 0.74 | -4.6 | -5.6 | -0.165 | 338.8
 |  | 98 | 0.12 | -4.6 | -6.3 | -0.265 | 339.6
5 | Displaced QF | 135 | 0.62 | -6.0 | -8.4 | -0.095 | 304.0
 |  | 84 | 0.14 | -6.1 | -7.7 | -0.215 | 304.0

## Slide 31: lattice combining options 4a and 5
e = 106pm Qx = 52.27 Qy = 16.35
= 1.08e-4 𝜉x = -189 𝜉y = -53
C = 307.6m 𝜉x /Qx = ~3.6 𝜉y /Qy = ~3.2
L = 15.38m
5-bend MBA with 20 straight sections, TG in main bend and displaced QF (RB)
Input (MBA-cell):
Half length dipole: 40cm
Half angle dipole: 2.3°, 0.84T
  K = -2.25, 18.8T/m
Displaced QF: 0.13m
  K=11.1, 92T/m
  -0.205°, Dx~2.5mm
bx = 0.103m
by =8m
h = 0.0058m

## Slide 32: lattice combining options 4a and 5
Dynamic Aperture – stage 0 – 1000 turns
Qx=52.27, 16.35
Chromaticity tuned to +2
bx = by = 1.5m
6 SX families: SD/SF in MBA cell
        SD/SF in matching cell
        S3,S4 in straight section
OPA – optimization tune shift terms
=> Promising start for optimization
@ center of
straight section
bx = 1.5m
by = 1.5m
Use values of Soleil upgrade
injection straight:
bx = 11m
by = 3m
Soleil goal: Ax = 6mm
Ay = 2.5mm
SLS2: Ax,y < 4mm
All straights
11m / 3m

## Slide 33: lattice combining options 3 and 5
 | Results for full lattices | e [pm] | a [e-4] | x/ Q x | x/ Q y | q RB | Circ. [m]
 | reference | 105 | 0.14 | -5.7 | 7.8 | -0.205 | 321.2
1 | Relax h0 | 140 | 0.52 | -5.7 | -8.7 | -0.110 | 321.2
2 | Relax b0 | 139 | 0.06 | -3.6 | -3.9 | -0.235 | 322.8
3 | Increase L | 135 | 0.74 | -4.6 | -6.2 | -0.165 | 339.6
4a | Increase L + TG | 134 | 1.01 | -3.8 | -3.4 | -0.205 | 318.8
4b | Increase L (+LG) | 142 | 0.74 | -4.6 | -5.6 | -0.165 | 338.8
 |  | 98 | 0.12 | -4.6 | -6.3 | -0.265 | 339.6
5 | Displaced QF | 135 | 0.62 | -6.0 | -8.4 | -0.095 | 304.0
 |  | 84 | 0.14 | -6.1 | -7.7 | -0.215 | 304.0

## Slide 34: lattice combining options 3 and 5
5-bend MBA with 20 straight sections, long bend and displaced QF (RB)
Input (MBA-cell):
Half length dipole: 40cm
Half angle dipole: 2.22°, 0.81T
Displaced QF: 12cm
  K=11.4, 95T/m
  -0.125°, Dx~1.6mm
bx = 0.103m
by =12m
h = 0.0058m
e = 120pm Qx = 53.25 Qy = 11.35
= 1.00e-4 𝜉x = -233 𝜉y = -71
C = 321.5m 𝜉x /Qx = ~-4.4 𝜉y /Qy = ~-6.3
L = 16.08m
=> as close to separated function as possible

## Slide 35: lattice combining options 3 and 5
Dynamic Aperture – stage 0 – 1000 turns
Qx=53.25, 11.35
Chromaticity tuned to +2
bx = by = 1.5m
6 SX families: SD/SF in MBA cell
        SD/SF in matching cell
        S3,S4 in straight section
OPA – optimization tune shift terms
=> Promising start for optimization
@ center of
straight section
bx = 1.5m
by = 1.5m

## Slide 36: lattice combining options 4b and 5
 | Results for full lattices | e [pm] | a [e-4] | x/ Q x | x/ Q y | q RB | Circ. [m]
 | reference | 105 | 0.14 | -5.7 | 7.8 | -0.205 | 321.2
1 | Relax h0 | 140 | 0.52 | -5.7 | -8.7 | -0.110 | 321.2
2 | Relax b0 | 139 | 0.06 | -3.6 | -3.9 | -0.235 | 322.8
3 | Increase L | 135 | 0.74 | -4.6 | -6.2 | -0.165 | 339.6
4a | Increase L + TG | 134 | 1.01 | -3.8 | -3.4 | -0.205 | 318.8
4b | Increase L (+LG) | 142 | 0.74 | -4.6 | -5.6 | -0.165 | 338.8
 |  | 98 | 0.12 | -4.6 | -6.3 | -0.265 | 339.6
5 | Displaced QF | 135 | 0.62 | -6.0 | -8.4 | -0.095 | 304.0
 |  | 84 | 0.14 | -6.1 | -7.7 | -0.215 | 304.0
Not successful: e = 144pm , a= 1.04e-4

## Slide 37: lattice combining options 4A and 4b
 | Results for full lattices | e [pm] | a [e-4] | x/ Q x | x/ Q y | q RB | Circ. [m]
 | reference | 105 | 0.14 | -5.7 | 7.8 | -0.205 | 321.2
1 | Relax h0 | 140 | 0.52 | -5.7 | -8.7 | -0.110 | 321.2
2 | Relax b0 | 139 | 0.06 | -3.6 | -3.9 | -0.235 | 322.8
3 | Increase L | 135 | 0.74 | -4.6 | -6.2 | -0.165 | 339.6
4a | Increase L + TG | 134 | 1.01 | -3.8 | -3.4 | -0.205 | 318.8
4b | Increase L (+LG) | 142 | 0.74 | -4.6 | -5.6 | -0.165 | 338.8
 |  | 98 | 0.12 | -4.6 | -6.3 | -0.265 | 339.6
5 | Displaced QF | 135 | 0.62 | -6.0 | -8.4 | -0.095 | 304.0
 |  | 84 | 0.14 | -6.1 | -7.7 | -0.215 | 304.0
Not successful: e = 151pm , a= 1.04e-4

## Slide 38
lattice combining options 4a and 5
5-bend MBA with 20 straight sections, TG in main bend and displaced QF (RB)
+ space for vacuum and adjusted sextupole length
e = 104pm Qx = 52.25 Qy = 16.35
= 1.04e-4 𝜉x = -176 𝜉y = -57
C = 318.4m 𝜉x /Qx = ~3.4 𝜉y /Qy = ~3.5
= +10cm; 0.4m*20= 8m
End of identical MBA-cellls

## Slide 39: List of magnets
magnet | Length [m] | Angle [°] | Field [T] | K [1/m²] | Gradient [T/m] | B’’/2Br [1/m³] | SX [T/m²]
main bend | 0.80 | 4.74 | 0.86 | -2.2 | 18.3 |  | 
displaced QF | 0.12 | 0.215 | 0.26 | 11.7 | 97.5 |  | 
Q1A | 0.09 |  |  | 4.4 | 36.7 |  | 
MQ2 | 0.09 |  |  | 9.7 | 80.8 |  | 
MQ1 | 0.09 |  |  | -2.8 | -23.3 |  | 
UQ1 | 0.17 |  |  | -11.2 | -93.3 |  | 
UQ2 | 0.26 |  |  | 11.2 | 93.3 |  | 
UQ3 | 0.09 |  |  | -10.9 | 90.8 |  | 
S1 | 0.10 |  |  |  |  | -793.0 | -13216
S0 | 0.14 |  |  |  |  | 789.8 | 13162
S1A | 0.08 |  |  |  |  | -157.9 | -2631
S0A | 0.10 |  |  |  |  | 871.0 | 14516
S3 | 0.08 |  |  |  |  | -568.9 | -9481
S5 | 0.08 |  |  |  |  | 302.9 | 5048
E/0.3 = B*r = 8.333

## Slide 40: List of lattice options
 | lattice | # of bends | periods | Circum- ference [m] | e [pm] | a [e-4]
 | reference | 5 | 20 | 321.2 | 105 | 0.14
1 | Long main dipole w/o gradient and displaced QF | 5 | 20 | 321.5 | 120 | 1.00
2 | Transverse gradient in main bend and displaced QF | 5 | 20 | 307.6 | 106 | 1.08
3 | Transverse gradient in main bend and displaced QF | 7 | 16 | 307.8 | 67 | 1.05
4 | Transverse gradient in main bend and displaced QF | 5 | 16 | 240.6 | 158 | 0.99
Fall back solution without magnet-technological challenges
Most efficient solution
Most inefficient solution, unless e << 100pm is needed
  816 magnets  780 magnets for 20 periods
Tough, but feasible…(i.e. permanent magnet as matching dipole...)
BIII in BII-tunnel ?
Length of beamlines?
Shielding (1.7->2.5GeV)?
Vibrations?

## Slide 41: Conclusion
Conclusion:
The bottleneck for the lattice development is the momentum compaction factor
We need to agree on what we think is the appropriate limit on a
Going to a ~ 6e-5 would open lots of possibilities for the lattice design
For a > 1e-4 we need to utilize combined function magnets
The methodology presented led to two lattice options with 20 straight sections
  on ~ 300m circumference, that fulfill the considered requirements
  and should be further investigated
We should specialize within the group to be more efficient
Next steps: confirm opa results with elegant/MAD
  off momentum properties
  rudimental hardware check (vacuum, magnets, magnet-apertures…)
  injection
  ….
Thank you for your attention!

## Slide 42: 7-bend achromat, 16 periods, 300 m

## Slide 43: 7-bend achromat, 16 periods

## Slide 44: 7-bend achromat, 16 periods, 240 m

## Slide 45: Grundstücksgröße
=> Die benötigte Grundstückgröße ist 2x Länge der Beamlines